## Slide 1: Network Protocols
Rules and procedures for transmitting data across a network
Hope you’re ready for
ACRONYMS!

## Slide 2: The OSI Model
Stands for Open Systems Interconnection
Separates network communication into 7 layers of abstraction:
Physical Layer – Electronic circuit transmission (as in bits, not full packets of data)
  Examples: USB, Bluetooth
Data Link Layer – Responsible for transferring data between network nodes
  Examples: Ethernet, ARP
Network Layer – Packets are forwarded here in a process known as routing
  Examples: IPv4, IPv6
Transport Layer – Host-to-host communication
  Example: TCP
Session Layer – Manages session between end-user application processes
Presentation Layer – Data translation
Application Layer – Displays information received to the user
  Examples – DNS, HTTP, FTP

## Slide 3: Most common protocols you will encounter
TCP/IP
ARP
DHCP
DNS
FTP (SFTP/TFTP)
HTTP (HTTPS)

## Slide 4: TCP and IP
TCP
Transmission Control Protocol
Delivers bytes between applications running on hosts
IP
Internet Protocol
Responsible for routing from a source host to a destination host across one or more IP networks by using an addressing system
*cough* hence the name IP Address *cough*

## Slide 5: ARP
Address Resolution Protocol
Responsible for discovering MAC (media access control) address
In Wireshark ARP packets are usually read as “Who has #.#.#.#? Tell #.#.#.#”
This means that the IP address after the ‘Tell’ part knows it wants to send data to the IP address after the ‘Who has’ part but it does not know the MAC address yet

## Slide 6: DHCP
Dynamic Host Configuration Protocol
Responsible for dynamically assigning IP addresses and any other necessary parameters to each device on a network

## Slide 7: DNS
Domain Name System
Translates memorized domain names into numerical IP addresses
Cloudflare’s 1.1.1.1 is a great alternative to your ISPs DNS resolver
Consider building a Pi-Hole to use as your DNS server

## Slide 8: FTP
File Transfer Protocol
Uses ports 20 and 21
Used to transfer files between a client and a server (imagine that)
This was not designed to be a secure protocol, so SFTP (SSH File Transfer Protocol, using port 22) is a better solution
TFTP (port 69) stands for Trivial File Transfer protocol and is used to quickly transfer small files (there is no authentication)

## Slide 9: HTTP
Hypertext Transfer Protocol
Uses port 80
The foundation of communication for the World Wide Web
This is what actually transfers the website to the user in the form of instructions like a text document
HTTPS (Hypertext Transfer Protocol Secure, using port 443) is an extension of HTTP which is encrypted with TLS (Transfer Layer Security)

## Slide 10: More HTTP
HTTP utilizes several methods such as:
  POST – Create an entry
  GET – Read an entry
  PUT – Update an entry
  DELETE – Delete an entry
  And many more
The first line of an HTTP response is the status code, which can indicate one of 5 things:
  100 – Info
  200 – Success
  300 – Redirection
  400 – Client error
  500 – Server error

## Slide 11: BONUS PROTOCOL!
TELNET (Teletype Network, port 23)
Establishes remote terminal connection for bidirectional text based communication
This allows the user of one computer to log into another computer on the network
Enter this into the terminal: `telnet towel.blinkenlights.nl`
  If that does not work do this: `brew install telnet`
  If that does not work do this: `/usr/bin/ruby –e “$(curl –fsSL https://raw.githubusercontent.com/Homebrew/install/master/install)”`
BONUS FACT! SSH (Secure Socket Shell, port 22) is basically just secure TELNET

## Slide 12: BONUS PROTOCOL AGAIN (last slide I promise)
H.323
Uses ports 1720 and 1721
Used for video conferences
SIP
Uses ports 5060 and 5061
Used for computer-telephone (audio conferences)
TIME 4 LAB